## Slide 1: Building a Trusted Environment on RISC-V
TEAM 42
NSU-FIT 2025

## Slide 2: Reflections on Trusting Trust
Modern programs are compiled by other programs (compilers).
If the compiler is compromised, even clean source code does not guarantee security.
A backdoor can persist across generations.
$ gcc → a compiler written in C
The C compiler is built… by another compiler
We trust tools that may themselves be compromised.
What if the backdoor is not in the program, but in the compiler itself?

## Slide 3: Concept of the Trusted Chain
|> How can we verify that a compiler is compromised?
gcc-infected
trusted compiler
gcc.c
gcc-infected
Trusted
gcc
gcc
gcc
The Diverse Double Compilation (DDC) method is used:
the compiler is built using two independent systems and the results are compared.
If the results are identical, the compiler is considered trusted.

## Slide 4
|> Goal — build a trusted
| computing chain
Project goals
The main idea is to obtain a system where every file can be verified by a human.
Starting from minimal assembly code, understandable to the eye,
and gradually building the tools.
Assembler
↓
Compiler (Stage 1)
↓
Compiler (Stage 2)
↓
Kernel (Stage 3)
↓
C standard library
↓
Kernel (Linux)
“We cannot trust a system if we cannot verify its foundations.” — Ken Thompson, Reflections on Trusting Trust

## Slide 5: Winter school YADRO
|> The main goal of the ws25-bootstrap | project is a minimal boot environment | for RISC-V.
Implemented:
initial bootloader (stage1)
UART output
payload in the form of a “Hello, world!” program
$ qemu-system-riscv64 \
-machine virt \
-bios stage1.bin
Boot sequence: stage1 → stage2
Hello, world!
# `qemu-system-riscv64` emulates a 64-bit RISC-V processor
(virt — a virtual machine not bound to a specific SoC)

## Slide 6: Project architecture
┌──────────────┐
│ Stage 1 (ASM) │ → initializes registers, UART, prints ‘Hello world’
└──────────────┘
↓
┌──────────────┐
│ │ Provides a higher-level execution layer
│ Stage 2 (C) │ → (e.g. user output, stack preparation),
│ │ transfers control to the kernel
└──────────────┘
↓
┌──────────────┐
│ Kernel │ → Performs kernel loading and memory management
└──────────────┘
Each stage is written in the language of the previous level
Binaries can be manually verified (short, transparent)
The build is reproducible

## Slide 7
Kernel
What will we work on?
Our goal is to implement a boot chain that prepares the system to launch the kernel.
We are creating a minimal bootloader that:
Initializes memory and UART,
Transfers control to the next stage,
works without external libraries or dependencies,
can be read and verified by a human.
Boot
We are developing a minimal system kernel running on RISC-V
that performs basic OS functions:
Memory management,
System calls,
Multitasking and interrupts,
Interaction with I/O devices.
Our task is to build a kernel that can be compiled
using only trusted code from the previous stages (boot).

## Slide 8
Step-by-step plan
1) Stage 1 — System bring-up (QEMU, ASM)
Write minimal ASM code
Set up stack and essential registers
Initialize UART and print “Hello from Stage 1”
Produce ELF→BIN and hand off control to Stage 2 at a fixed address
2) Stage 2 — C runtime & hand-off
Print a line via UART using C functions
Initialize a tiny C runtime (.bss/.data, simple init)
Prepare execution context for the kernel entry
Transfer control to the kernel stub (Stage 3)
3) Stage 3 — Minimal kernel (kernel stub)
Define kernel entry address and linker script
Basic memory management (simple allocator), trap/interrupt vector
Minimal system call stub(s) and timer/interrupt handling
(Optional) cooperative task loop to demonstrate scheduling
Diverse Double Compilation (DDC) — trust verification
Build the toolchain/artifacts via two independent paths/environments
Compare SHA256 of key artifacts; identical results → trusted
Hardware boot — Lichee Pi 4A
Adapt payload for the board (UART params, memory map, DT if needed)
SD-card boot preparation and console bring-up
Verify “Hello”/kernel log over UART on real hardware
Packaging & documentation
Lock external tool versions; provide `make qemu`, `make hw`, `make verify`
Publish Memory Map, SRS, Vision, Project Schedule
Stage 1 → Stage 2 → Stage 3 → Hardware Boot → Verification